## Slide 1: Floating
LESSON 5

## Slide 2: Fractional Binary Representation
Digits to the left of the binary point have weights of the form 2i, while those to the right have weights of the form 1/2i.

## Slide 3: Fractional Binary Numbers: Examples
Value Representation
101.112
010.1112
001.01112
Observations
  Divide by 2 by shifting right(unsigned)
  Multiply by 2 by shifting left
  Numbers of form 0.11111……2 are just below 1.0
    1/2 + 1/4 + 1/8 + …… 1/2i → 1.0
    Use notation 1.0 - ε

## Slide 4: Representable Numbers
Limitation #1
  Can only exactly represent numbers of the form x/2k
    Other rational numbers have repeating bit representations
  Value Representation
    1/3 0.0101010101[01]…2
    1/5 0.001100110011[0011]…2
    1/10 0.0001100110011[0011]…2
    Limitation #2
  Just one setting of decimal point within the w bits
    Limited range of numbers (very small values? very large?)

## Slide 5: Encoding Rational Numbers（有理数）
Form
Very useful when or
An Approximation to real arithmetic
From programmer’s perspective
  Uninteresting
  Arcane （神秘的）and incomprehensive （难以理解的）
Notes: 对于表示非常大的数字，非常接近0的数字，以及作为实数运算的近似值非常有用。

## Slide 6: History & Features
Until 1980s
  Many idiosyncratic （特殊的） formats
IEEE Standard 754
  Established in 1985 as uniform standard for floating point arithmetic
  Designed by W. Kahan for Intel processors
  Supported by all major CPUs
  Driven by numerical concerns
  Nice standards for rounding, overflow, underflow
  Try hard to make fast in hardware
    Numerical analysts predominated over hardware designers in defining standard
Notes: fast speed, easy implementation, less accuracy

## Slide 7: Floating Point Representation
Numerical Form：
  Sign bit s determines whether number is negative or positive
  Significand M normally a fractional value in range [1.0,2.0)
  Exponent E weights values by power of two
  Encoding：
  MSB s is sign bit s
  exp field encodes E and is presented by frame shit (移码) (but is not equal to E)
  frac field encodes M and is presented by magnitude (原码) (but is not equal to M)
Notes: Significand 尾数
Exponent 阶码，2E表示浮点数的阶，E为阶码

## Slide 8: Precision options
Single precision: 32 bits
Double precision: 64 bits
Extended precision: 80 bits (Intel only)
Notes: 给定浮点数编码格式后，根据exp的值，浮点数取值有三种不同的情况：规格化的值、非规格化的值以及特殊值（无穷大或非数）

## Slide 9: “Normalized” Values
When: exp ≠ 000…0 and exp ≠ 111…1
Exponent coded as a biased value (偏置) : E = exp – Bias
  exp: unsigned value exp
  Bias = 2k‐1 - 1,where k is number of exponent bits
    Single precision: 127 (exp: 1…254, E: ‐126…127)
    Double precision: 1023 (exp: 1…2046, E: ‐1022…1023)
    Significand coded with implied leading 1: M = 1.xxx….x2
  xxx…x: bits of frac
  Minimum when frac = 000…0 (M = 1.0 )
  Maximum when frac = 111…1 (M = 2.0 - ε)
  Get extra leading bit for “free”
Notes: 阶码非全零或全1. 此时阶码被解释为以偏置形式表示的有符号数。
规格化的尾数小数点在最高有效位左边，并且总是1，故尾数值为[1, 2)。但1总被隐去（隐藏位），因此23位尾数表示的实际上是24位有效数字。
通过调整解码，可以很方便的将尾数调整为规格化的表示，即取值在大于等于1，小于2的范围内。

## Slide 10: Single Precision Exponent Coding (frame shit)
E (exponent value) | exp (two’s complement) | exp (frame shit)
-12610 | 1000 0010 | 0000 0001
-12510 | 1000 0011 | 0000 0010
. . . . | . . . . | . . . .
-110 | 1111 1111 | 0111 1110
010 | 0000 0000 | 0111 1111
110 | 0000 0001 | 1000 0000
210 | 0000 0010 | 1000 0001
. . . . | . . . . | . . . .
12710 | 0111 1111 | 1111 1110
阶码采用移码编码，按照无符号数解释时，阶码编码排序与阶码值排序一致，便于阶码比较（对阶）

## Slide 11: Normalized Encoding Example
Value: float f = 15213.0
  1521310 = 111011011011012
  = 1.11011011011012 × 213
  Significand：
  M = 1.11011011011012
  frac = 110110110110100000000002
  Exponent：
  E = 13
  bias = 127
  exp = 140 = 100011002
  Result

## Slide 12: Normalized Encoding Practice (1)
Value: float f = -0.75
  -0.7510 = -0.112
  = -1.12 × 2-1
  Sign:
  s = 1
  Significand：
  M = 1.12
  frac = 1000 0000 0000 0000 0000 0002
  Exponent：
  E = -1
  bias = 127
  Exp = 126 = 0111 11102
  Result:
  1 0111 1110 1000 0000 0000 0000 0000 000  0xBF400000

## Slide 13: Normalized Encoding Practice (2)
求IEEE 754单精度浮点数0xC0A00000的值是多少？
0xC0A00000 = 1 10000001 0100 0000 0000 0000 0000 0002
  Sign:
  s = 1
  Significand：
  frac = 0100 0000 0000 0000 0000 0002
  M = 1.012 = 1.2510
  Exponent：
  exp = 1000 00012 = 12910
  bias = 127
  E = 129 – 127 = 2
  Result:
  (-1)1 × 1.25 × 22 = -5.0

## Slide 14: “Denormalized” Values
Condition: exp = 000…0
Exponent value: E = - Bias + 1 (insteads of E = 0 - Bias)
Significand coded with implied leading “0”(Not “1”): M = 0.xxx…x2
  xxx…x: bits of frac
  Case: exp = 000…0, frac = 000…0
  Represents zero value
  Note distinct values: +0 and -0 (why?)
  Case: exp = 000…0, frac ≠ 000…0
  Numbers closest to 0.0
  Equispaced (等间距的)
Notes: 非规格化值有两个用途：表示数值0和非常接近于0的数值
用于处理阶码下溢。当运算结果的阶太小（小于-126）时，尾数右移，阶码加1，如此循环直到尾数为0或阶达到最小值，该过程称为“逐级下溢”

## Slide 15: Special Values
Condition: exp = 111…1
Case: exp = 111…1, frac = 000…0
  Represent value ∞ (infinity)
  Operation that overflows
  Both positive and negative
  E.g., 1.0/0.0 = -1.0/-0.0 = + ∞, 1.0 / -0.0 = - ∞
  Case: exp = 111…1, frac ≠ 000…0
  Not-a-Number (NaN)
  Represents case when no numeric value can be determined
  E.g., ∞ - ∞，∞ × 0
Notes: 引入无穷大使得在计算过程中出现异常的情况下程序能继续进行下去。

## Slide 16: Categories of single-precision floating-point values
Notes: 规格化
非规格化

## Slide 17: Visualization: Floating Point Encodings

## Slide 18: Tiny Floating Point Example
8-bit Floating Point Representation
  The sign bit is in the most significant bit
  The next four bits are the exponent, with a bias of 7
  The last three bits are the frac
  Same general form as IEEE Format
  normalized, denormalized
  represenation of 0, NaN, infinity

## Slide 19: Dynamic Range (Positive Only)
Notes: 8位浮点数的非负值情况
最大非规格化数和最小规格化数之前平滑转变（否则，非规划化数的阶值都是1/128）

## Slide 20: Interesting Numbers
参照该表，请推出最小/最大非规格化负数、最小/最大规格化整数、-1的数值表达式。假设尾数部分位宽为n，阶码位宽为k。（作为本章作业）
Notes: 1. 最小的正非规格化数：最低有效位（尾数最低有效位）为1，其余位均是0。尾数值M=2-n，阶码值E=-2k-1+2。数字值V = 2-n-2^(k-1)+2
2. 最大的正非规格化数：阶码字段均是0，尾数字段全是1。尾数值M=(1-2-n)，阶码值E=-2k-1+2。数字值V = (1-2-n)*2-2^(k-1)+2
3. 最小的正规格化数：阶码字段最低有效位是1，尾数字段全是0。尾数值M=1，阶码值=-2k-1+2。数字值V = 2-2^(k-1)+2
4. 最大的正规格化数：阶码字段最低有效位是0，其余都是1；尾数字段全1。尾数值M=2-2-n，阶码值 = 2k-1-1。数字值V=(2-2-n)*(22^(k-1)-1)

## Slide 21: Distribution of values
2-126
2-125
2-124
2-123
1.0…0x2-126~ 1.1…1x2-126
0.0…0x2-126~ 0.1…1x2-126
2-126
2-125
2-124
2-123
0
0
GAP
Normalized numbers
Denorms
(-1)s×0.xx…x ×2-126
Notes: 越靠近原点越稠密

## Slide 22: Special Properties of the IEEE Encoding
FP Zero Same as Integer Zero
  All bits = 0
  Can (Almost) Use Unsigned Integer Comparison
  Must first compare sign bits
  Must consider -0 = 0
  Nans problematic
    Will be greater than any other values
  Otherwise OK
    Denormalized vs. Normalized
    Normalized vs. Infinity

## Slide 23: Round （舍入）Mode
Mode | 1.40 | 1.60 | 1.50 | 2.50 | -1.50
Round-to-Even | 1 | 2 | 2 | 2 | -2
Round-toward-zero | 1 | 1 | 1 | 2 | -1
Round-down | 1 | 1 | 1 | 2 | -2
Round-up | 2 | 2 | 2 | 3 | -1
Notes: 由于在计算机中浮点数的编码字长有限，因此浮点数的表数范围和精度也都受限，因此浮点数只能近似地表示实数。因此，对于一个实数值，我们希望可以找到一个最接近它的，并可以用浮点形式表示的匹配值，这一过程被称为舍入。对于每一个待舍入的值，根据舍入精度，我们都可以找到它的舍入上界和下界，因此舍入的关键在于舍入方向的确定。IEEE提供了4中输入方法。
Even: 向偶数，最低位为偶数
Zero: 向零方向 （负数向大，正数向小）
Down: 向小的数
Up: 向大的数

## Slide 24: Round Mode
Round down:
  rounded result is close to but no greater than true result.
Round up:
  rounded result is close to but no less than true result.
Round to Zero
  rounded result is close to 0.
  if positive, round result is no greater than true result
  otherwise, no less than true result.
Round to Even (Default Rounding Mode)
  half-way may be round up or round down
  the least significant digit of rounded result (half-way) must be even
  others are rounded to the nearest bound
Notes: 浮点数的表示方法限制了浮点数的范围和精度，所以浮点运算只能近似地表示实数运算。对于值x，我们希望找到能够用确定浮点格式表示的、最接近的比配值x’，这就是所谓的舍入。
问题的关键是舍入的方向。

## Slide 25: Round-to-Even
Applying to Other Decimal Places
  When exactly halfway between two possible values
    Round so that least significant digit is even
  E.g., round to nearest hundredth
    1.2349999 1.23 (Less than half way)
    1.2350001 1.24 (Greater than half way)
    1.2350000 1.24 (Half way—round up)
    1.2450000 1.24 (Half way—round down)

## Slide 26: Rounding Binary Number
“Even” when least significant bit is 0
Half way when bits to right of rounding position = 100…2
Value | Binary | Rounded | Action | Round Decimal
2 3/32 | 10.00011 | 10.00 | Down | 2
2 3/16 | 10.0011 | 10.01 | Up | 2 1/4
2 7/8 | 10.111 | 11.00 | Up | 3
2 5/8 | 10.101 | 10.10 | Down | 2 1/2
Notes: 舍入到百分位

## Slide 27: Round Practice
根据舍入到偶数规则，给出如下二进制小数舍入到小数点右边1位（ 1/2 位）。
A. 10.010
B. 10.011
C. 10.110
D. 11.001
10.0（正中间）
10.1
11.0（正中间）
11.0

## Slide 28: Floating Point Operations: Basic Idea
Basic idea
  First compute exact result
  Make it fit into desired precision
    Possibly overflow if exponent to large
    Possibly round to fit into frac

## Slide 29: Floating Point Multiplication
(-1)s1 M1 2E1 × (-1)s2 M2 2E2 （参与运算的两个浮点数均是规格化浮点数）
Exact Result: (-1)s M 2E
  Sign s: s1^s2
  Significand M: M1 ×M2
  Exponent E: E1 + E2
  Fixing（规格化）
  If M ≥ 2, shift M right, increment E
  If E out of range, overflow
  Round M to fit frac precision
  Implementation
  Biggest chore（繁琐） is multiplying significands

## Slide 30: Floating Point Addition
(-1)s1 M1 2E1 + (-1)s2 M2 2E2
  Assume E1 > E2
Exact Result: (-1)s1 M 2E
  Sign s, Significand M : Result of signed align & add
  Exponent E: E1（尾数右移，小阶向大阶对齐）
  Fixing（规格化）
  If M ≥ 2, shift M right, increment E（右规，尾数只需右移1次）
  If M < 1, shift M left k positions, decrement E by k（左规）
  Overflow if E out of range
  Round M to fit frac precision

## Slide 31: Floating Point Addition Example
例：用二进制浮点数形式计算 0.5 +(– 0.4375) =？
对 阶: -1.110 x 2-2 → -0.111 x 2-1
加 减: 1.000 x 2-1 +( -0.111 x 2-1 ) = 0.001 x 2-1
左 规: 0.001 x 2-1 → 1.000 x 2–4
判溢出: 无
解：0.5 = 1.000 x 2-1， - 0.4375 = -1.110 x 2-2
结果为： 1.000 x 2–4 = 0.0001000 = 1/16 = 0.0625
0.4375=0.25+0.125+0.0625=0.0111B

## Slide 32: Floating Point in C
C Guarantees Two Levels
  float single precision
  double double precision
  Conversions/Casting
  Casting between int, float and double changes bit representation
  double/float → int
    Truncates fractional part
    Like rounding toward zero
    Not defined when out of range
  int → double
    Exact conversion, as long as int has ≤ 53 bit word size
  int → float
    Will round according to rounding mode

## Slide 33: Floating Point in C
int x = …;
float f = …;
double d = …;
Assume neither d nor f is NaN or infinity

## Slide 34: Floating Point in C
x == (int)(float) x No: 24 bit significand
x == (int)(double) x Yes: 53 bit significand
f == (float)(double) f Yes: increases precision
d == (float) d No: loses precision
f == -(-f); Yes: Just change sign bit
2/3 == 2/3.0 No: 2/3 == 0
d < 0.0  ((d*2) < 0.0) Yes!
d *d >= 0.0 Yes!
(d+f)-d == f d = 1.0*230，f = 1.0，对阶后f = 0

## Slide 35: Example: Ariana Rocket Explode
1996年6月4日，Ariana 5火箭初次航行，在发射仅仅37秒钟后，偏离了飞行路线，然后解体爆炸，火箭上载有价值5亿美元的通信卫星。
原因是在将一个64位浮点数转换为16位带符号整数时，产生了溢出异常。溢出的值是火箭的水平速率，这比原来的Ariana 4火箭所能达到的速率高出了5倍。在设计Ariana 4火箭软件时，设计者确认水平速率决不会超出一个16位的整数，但在设计Ariana 5时，他们没有重新检查这部分，而是直接使用了原来的设计。
在不同数据类型之间转换时，往往隐藏着一些不容易被察觉的错误，这种错误有时会带来重大损失，因此，编程时要非常小心。

## Slide 36: Questions
Why ?
    1
Accuracy & Precision

## Slide 37: Homework & Lab
作业：
已上传至智慧树，请电子版提交，截止时间：10月9日晚23:59
实验：
已上传至智慧树，按实验指导书要求提交，截止时间：10月9日晚23:59
实验1分为两部分，先布置第一部分。